## Slide 1: Visualization
The Visualization Pipeline
Human Factors
Data Description
Classification of Visualization Methods
Visualization of Multiparameter Data

## Slide 2
In general, the content of all slides can be asked in the exam.
Some content is very likely to be asked in the exam. Marked with this sign:
Some content will not be asked. Marked with this sign:
very important
exam

## Slide 3: The Visualization Pipeline

## Slide 4: The Visualization Pipeline
The process of converting data to images contains the steps: Filtering, Mapping, Rendering
simulation
data bases
sensors
raw data
vis data
renderable representation
images, video
filtering
mapping
rendering
interaction
data acquisition
The Visualization Pipeline
very important

## Slide 5: The Visualization Pipeline
Filtering:
starts with raw data
raw data is prepared for the visualization
result is filtered data which go to the mapping step
 data to data map
filtering
mapping
rendering
data
image

## Slide 6: The Visualization Pipeline
Operations for filtering:
  completing the data set
    if data values are missing
    by interpolation
  reduce data set
    remove non-relevant data by certain criteria
  smoothing data
    apply filter and smoothing operators
  compute characteristic properties of the data
    gradients
    extreme values
    metadata
  apply conversions
filtering
mapping
rendering
data
image

## Slide 7: The Visualization Pipeline
Mapping:
conversion of the data into renderable 2D or 3D graphical primitives and their attributes (e.g. creating a polygon list or a triangular mesh)
consider expressiveness, effectiveness, appropriateness
 data to geometry map
filtering
mapping
rendering
data
image

## Slide 8: The Visualization Pipeline
To find good mappings, theories, algorithms and guidelines from different disciplines are used:
  computer graphics
  computer vision
  perception theory
  user interface design
  information processing
  psychology
  arts
filtering
mapping
rendering
data
image

## Slide 9: The Visualization Pipeline
Rendering:
Generating a 2D image, video, stereo image
 geometry to image map
filtering
mapping
rendering
data
image

## Slide 10: The Visualization Pipeline
Data flow in the Visualization pipeline

## Slide 11: The Visualization Pipeline
The visualization pipeline can be processed in a distributed environment, which gives the following distinction:

## Slide 12: The Visualization Pipeline
Reference model for Visualizations (Robertson):

## Slide 13: Visualization Scenarios

## Slide 14: Visualization Scenarios
How strong is the visualization connected to the creation of the data?

## Slide 15: Visualization Scenarios
Movie mode:
3) analysis of the data in motion
1) data acquisition
2) creating a movie
Notes: Very well suited for visualizations that require lots of computation time due to e.g. very large data or time-consuming visualizations algorithms

## Slide 16: Visualization Scenarios
Tracking:
analysis is directly combined with modeling and simulation
no interactive data processing

## Slide 17: Visualization Scenarios
Interactive post-processing (most common):
2) visualization and interactive processing of the data
1) data acquisition

## Slide 18: Visualization Scenarios
Interactive steering:
analysis is directly combined with modeling, simulation and visualization; interactive feedback

## Slide 19: Visualization Scenarios
Interactive steering, an example:
  Generation of 3D geometries during simulation
  Geometry streaming to client, that can steer both visualization and simulation.
Tele-Immersion in Wide Area Networks
S. Olbrich, T. Weinkauf, A.Merzky, H.-C. Hege
DFN-funded project of RRZN & ZIB, 2001

## Slide 20: Visualization Scenarios

## Slide 21: Visualization Scenarios
Movie mode
- very low flexibility
+ low complexity
+ very low demands on viewing device
- high demands on data storage
disconnected from simulation
Tracking
- very low flexibility
+ low complexity
+ low demands on viewing device
+ low demands on data storage
connected to simulation
Interactive post-processing
+ high flexibility for Vis
+/- medium complexity
- high demands on viewing device
- high demands on data storage
disconnected from simulation
Interactive steering
+ high flexibility for Sim & Vis
- high complexity
- high demands on viewing device
+/- medium demands on data storage
connected to simulation

## Slide 22: Visualization Scenarios
Demands on data storage, an example:
Ahmed body
Block-structured grid with 52 blocks
Each block is a curvilinear grid
17 million grid cells in total
Temporal resolution: a particle needs 10000 time steps from front to back of the Ahmed body
DFG-funded SFB 557
Erik Wassen, TU Berlin, Germany
2008

## Slide 23: Visualization Scenarios
Demands on data storage, an example:
DFG-funded SFB 557
Erik Wassen, TU Berlin, Germany
2008
17 million grid cells
x 10000 time steps
x 7 variables
X 8 bytes per double
= 8.66 terra bytes
(60.62 TB for total 70000 time steps)
 Do not save every time step, not every variable, and not every block.

## Slide 24: The Visualization Pipeline
simulation
data bases
sensors
raw data
vis data
renderable representation
images, video
filtering
mapping
rendering
interaction
data acquisition
The Visualization Pipeline
Data Aspects
Human Factors
Visualization Methods
(focus of the class)

## Slide 25: Human Factors in Visualization

## Slide 26
„This is Van Gogh’s last painting before he committed suicide.“
Notes: Background information is important.
Note how the perception of the image changes with the additional knowledge of this painting being Van Gogh‘s last painting. While most of the time perception issues are not that dramatic in visualization we still need to be aware of the problem of humans interpreting images.
Remark: it‘s debatable whether this is actually van Gogh‘s very last painting but it was definitely one of his last.

## Slide 28: Color Blindness
The numeral "74" should be clearly visible to viewers with normal color vision.
Viewers with dichromacy or anomalous trichromacy may read it as "21“.
Viewers with achromatopsia may not see numbers.
From http://en.wikipedia.org/wiki/Color_blindness
Notes: Red/Green
• Lack of or mutations in red or green cones
• Genes located on the X chromosome (women have 2, men have 1)
• 10% of men, less than 1% of women
Blue/Yellow
• Equally found in men & women
• mutation in short wave cone

## Slide 29: Color Perception
Colors are perceived in the following way:
Notes: This is a general guideline and may not hold up in all instances.
Temperature:
What colors go with warm/hot?
What colors go with cold?
Taste:
Possible tastes: spicy, bitter, sweet
Colors? (red, green, yellow/pink)

## Slide 30: Color Perception
Colors are perceived in the following way:
Notes: This is a general guideline and may not hold up in all instances.
Temperature:
What colors go with warm/hot?
What colors go with cold?
Taste:
Possible tastes: spicy, bitter, sweet
Colors? (red, green, yellow/pink)

## Slide 31: Human Factors in Visualization
Bertin identifies 7 graphical primitives from which the images are built (6 + color = value, hue, saturation):

## Slide 32: Human Factors in Visualization
There is a variety of case studies about the perception of these primitives.
Here: a few more statements from T. Koop´s masters thesis, (TH-Darmstadt):
Size:
  Human eye can distinguish up to 20 different sizes using a ratio of 1:10 between the smallest and the biggest size.
  Differences in size are better perceived for dark surfaces.
Brightness:
  Human eye can distinguish between 60 – 70 gray levels.
  For representing nominal data only 5 – 6 levels should be used.

## Slide 33: Human Factors in Visualization
Color:
  Perception of colors should be considered ( see Mapping)
  Number of distinguishable color levels relates directly to the size of the colored surface.
  Diameter should be at least 1.5 mm to perceive color differences.
  Color perception also depends on the adjacent colors (color bleeding).
Saturation:
  Selecting property is best for pure (fully saturated) colors. Pure colors should be used for small surfaces which represent extreme values.
  Saturation differences are harder to perceive than brightness differences.

## Slide 34: Human Factors in Visualization
Orientation:
  Direction is best perceived for icons with a longish shape.
  Directions are well distinguishable if angle is chosen between 30° and 60°.
  Number of directions in a visualization is limited.

## Slide 35: Human Factors in Visualization
Shape:
  Map from shape to data is complicated.
  Shape is appropriate as visual metaphor.
  Shapes can be obtained by combinations, e.g.:
    ShapeVis enhanced spring model
    directions from star shaped coordinates

## Slide 36: Human Factors in Visualization
Texture:
  A collection of small objects is generally perceived as texture / pattern.
  A texture with few and isolated objects is associated with „less“; texture with many objects is associated with „many“.
Further rules:
  A difference of the shape of two objects can easier be perceived than a difference in the size.
  Contrast facilitates perception as well as a full-range lighting.
  Regular geometric shapes are easier perceivable than asymmetric shapes.
It is important,
  Not to overload the human visual system in a visual representation.
  Solutions: focus & context, or linking techniques.

## Slide 37: Data Description

## Slide 38: Data Description
What kind of data do you know?
Give examples!
Notes: Table / Spreadsheet (Excel) Scalar, Vector, Tensor Fields
Images (Photos)
Videos
Text
HTML, XML (Trees)
Graphs

## Slide 39: Data Description
Scientific data are [Brodlie 92], [Bergeron 93], [Wong 97]
  m-dimensional data, which are gathered in an
  n-dimensional observation space.
We distinguish between:
  independent variables: dimensions which define the observation space
   „multidimensional data“
  dependent variables: the parameters observed in the observation space
   „multivariate data“
Fundamental visualization aims for multiparameter data are:
  Which values attain the dependent variables?
  In which spatial context are these values given?
  In which temporal context are these values given?

## Slide 40: Data Description
Common way of describing multiparameter data: table in which independent and dependent variables are marked:

## Slide 41: Data Description
Observation space is actual space & time
  Often the case in physics, medicine, chemistry, geology, …
  Many numerical methods available (derivatives, interpolation, …)
  The class will concentrate on visualization methods for that kind of data, starting with the next lecture.
No specific prior on observation space
  Often the case with business data, data bases, abstract spaces, …
  Few general methods exist
  Many guidelines exist
  We will look into this area today.

## Slide 42: Classification Scheme for Visualization Methods

## Slide 43: Classification Scheme for Visualization Methods
static
dynamic
2D
3D
complete
partial

## Slide 44: Classification Scheme for Visualization Methods
2D vs. 3D
  2D:
    no projections or visibility computations
    data values easily identifiable
  3D:
    projections and visibility computations
    additional dimension for coding the data values
    natural 3D interpretation by using depth cues (e.g.: transparency, perspective, shadows, ...)

## Slide 45: Classification Scheme for Visualization Methods
2D vs. 3D
Combination opportunities
Example: positioning of an applicator in a medical volume data set by means of a 2D and 3D detailed view and a 3D overview

## Slide 46: Classification Scheme for Visualization Methods
static vs. dynamic
static:
    do not change automatically (changes are results of interactions)
    appropriate for getting quantitative statements
dynamic:
    change automatically
    time axis for coding additional information
    appropriate for showing continuous changes

## Slide 47: Classification Scheme for Visualization Methods
Static vs. Dynamic Visualizations
Example: Static and dynamic Treemap visualization of finance data (www.smartmoney.com/map-of-the-market/)
Notes: Bild:
-Zeigt Börsenentwicklungen über ein Jahr
-zwei Level: Industriesektoren und Firmen
-Rechteckgröße (Blattgröße) zeigt Marktkapitalisierung einer Firma: Aktienkurs * im Umlauf sich befindende Aktien der Firma
-Industriesektoren sind Nicht-Blattknoten
-Farben stellen Änderungen des Aktienkurses dar: rot  Rückgang, schwarz  unverändert, grün Wachstum
-Interkation: Details über einzelne Firmen durch Annotationen, Suche nach bestimmten Firmen, Wahl der Farbabbildung
Interpretation:
-starkes Wachstum ist anhand von hellen, grünen Rechtecken erkennbar
-Baumstruktur (Nicht-Blatt Knoten) durch graue Linien dargestellt, Linienbreite kodiert Baumtiefe

## Slide 48: Classification Scheme for Visualization Methods
complete vs. partial
complete:
    show all data in one image
    size of data set limited
partial:
    show subsets of data set
    requires interaction techniques to control the reduction
    without navigation or linking techniques: loss of information
    enables analyses of individual parts of the observation space and feature space

## Slide 49: Classification Scheme for Visualization Methods
Complete vs. Partial Visualizations
Example: Partial visualization of simulation data of a catalytic converter (Katalysator). Reduction is controlled by specifying features by means of linking and brushing. (From: Doleisch et al., 2003)
[From Doleisch et al., 2003]
Notes: Source:
http://www.vrvis.at/vis/research/fdl-vis/
Doleisch, Helmut; Gasser, Martin; Hauser, Helwig: "Interactive Feature Specification for Focus+Context Visualization of Complex Simulation Data.", In: Proceedings of the 5th Joint IEEE TCVG - EUROGRAPHICS Symposium on Visualization, VisSym‘03 (2003) 239-248

## Slide 50
Wednesday, 10.15: Coding tutorial
  Bring your laptop
  Clone Inviwo from Github (see Canvas)
  Cmake
  Qt

## Slide 51: Visualization of Multiparameter Data
No specific prior on observation space

## Slide 52: Visualization of Multiparameter Data
General Remarks and Classification
Aim: abstraction of properties of the observation space
while keeping
important correlations:
  values per observation point
  values per observation case
  values per dependent variable.

## Slide 53: Visualization of Multiparameter Data
First method: scatter plot
Cylinders | Horsepower (PS) | Weight (kg) | Origin
4 | 110 | 1576 | Germany
6 | 105 | 3535 | Japan
8 | 150 | 4190 | U.S.A.
Dimension A
Dimension B

## Slide 54: Visualization of Multiparameter Data
Classification for distinguishing basic technologies for visualization of multiparameter data
  panel matrices
  line sequences
  icon based techniques
  pixel based techniques
  hierarchical techniques

## Slide 55: Visualization of Multiparameter Data
Panel matrices
Idea: configuration of bivariate representations of the n-dimensional observation space in matrices
Examples: scatterplot matrices; prosection views; hyper slices
  scatterplot matrices (Cleveland 93)
  configuration of scatterplots in a matrix for showing different combinations of variables
  prosection views (Furnas, Buja, 1994)
  matrix of all orthogonal projections for specified regions of the observation space (prosection = combination of selections and projections)
  hyper slice (van Wijk, J. J., van Liere R. D., 1993)
  matrix of n2 slices through the n-dimensional observation space which intersect in a point of interest (current point) .
  (navigation in observation space possible by moving the current point.)

## Slide 56: Visualization of Multiparameter Data
Scatterplot matrix, Cleveland 93
configuration of scatterplots in a matrix for showing different combinations of variables

## Slide 57: Visualization of Multiparameter Data
Prosection Views
matrix of all orthogonal projections for specified regions of the observation space (prosection = combination of selections and projections)

## Slide 58: Visualization of Multiparameter Data
Hyper slice (van Wijk, J. J., van Liere R. D., 1993)
matrix of n2 slices through the n-dimensional observation space which intersect in a point of interest (current point). (navigation in observation space possible by moving the current point.)

## Slide 59: Visualization of Multiparameter Data
Line sequences
idea: mapping points of observation space to line sequences
examples:
  parallel coordinates,
  3D parallel coordinates,
  star shaped coordinates,
  parahistograms

## Slide 60: Visualization of Multiparameter Data
Parallel coordinates (Inselberg, 1990)
  n-dimensional parallel coordinate ­system in plane is defined by n parallel axes x1, x2, ..., xn
  A point P with the coordinates (p1, p2, ..., pn) in n-dimensional observation space is represented by a line sequence in parallel coordinates. This line sequence is defined by the points P1, P2, ..., Pn on the axes x1, x2, ..., xn of the parallel coordinate system. Pi lies on xi and has the coordinate pi (i = 1,2,...,n).
very important

## Slide 61: Visualization of Multiparameter Data

## Slide 62: Visualization of Multiparameter Data
microbiological data set using parallel coordinates

## Slide 63: Visualization of Multiparameter Data
Point-line duality for parallel coordinates
The point x in a) represented by the line sx in parallel coordinates in b).

## Slide 64: Visualization of Multiparameter Data
Point-line duality for parallel coordinates
  A straight line in the Cartesian coordinate system (a) is found as the intersection point of the lines in Parallel Coordinates (b). These lines in PC are defined by the sample points on the straight line.
    The intersection is not necessarily between X1 and X2
    An intersection point is not defined, if the slope of the straight line is 1, since then the lines in PC are parallel to each other.

## Slide 65: Visualization of Multiparameter Data
Conic-conic duality for parallel coordinates

## Slide 66: Visualization of Multiparameter Data
Curve-curve duality for parallel coordinates
Cusp <-> inflection point duality

## Slide 67: Visualization of Multiparameter Data
lines need space!

## Slide 68: Visualization of Multiparameter Data
Parallel coordinates (Inselberg, 1990)
for the visual analysis it is important to offer interaction tools, such as:
  reducing the number of axes;
  exchange axes;
  scaling axes;
  reducing the number of line sequences;
  emphasize particular line sequences.
Show live demo

## Slide 69: Visualization of Multiparameter Data
Brushing selections to select subsets
Car example (speed, cylinders, PS, weight, acceleration) from: [Telea, 2008]

## Slide 70: Visualization of Multiparameter Data
3D Parallel Coordinates:
  parallel planes instead of parallel axes; each plane is described by two axes; two variables can be mapped to each plane.
Weinkauf, Köller, University of Rostock, 1997

## Slide 71: Visualization of Multiparameter Data
Parahistograms (WINVIZ, Ong, Lee: 1996)
  extension of parallel coordinates by integrating histograms to show the number of data values.

## Slide 72: Visualization of Multiparameter Data
normal parallel
coordinates
“higher order parallel coordinates”
(shows correlations between (Horsepower, Weight, Displacement), (Displacement, Horsepower, Cylinders).
Higher order parallel coordinates (Theisel 01)
  Place additional coordinate axes between the “main” axes, use free-form-curves instead of straight line segments.
  Example: car data set: 6 dimensions, 38 objects.

## Slide 73: Visualization of Multiparameter Data
Properties of a company
using star shaped coordinates (Kiviatgraph)
Star shaped coordinates:
  similar to parallel coordinates but star shaped configuration of coordinate axes

## Slide 74: Visualization of Multiparameter Data
Example for star shaped coordinates

## Slide 75: Visualization of Multiparameter Data
Assessment of Parallel Coordinates and derived methods:
  good:
    lossless maps possible;
    both qualitative and quantitative statements possible;
    correlation between two dimensions well recognizable.
  bad:
    hard to trace particular line segments for large data sets (especially for parallel and star shaped coordinates)
    correlations between more than two dimensions are difficult to see

## Slide 76: Visualization of Multiparameter Data
Icon based techniques
  idea: visualization of data values as properties of icons / glyphs.  One icon represents the values of one observation case.
  There is no unique distinction between the names „icon“ and „glyph“ in the literature. In most cases they have the same meaning.
Glyphs/icons are geometric objects with the following properties:
  can be located at exact positions; these positions give spatial information.
  encode values of physical variables:
    in geometric characteristics like angle, length or shape,
    in attributes of the representation like color or transparency.

## Slide 77: Visualization of Multiparameter Data
Icons are used for encoding more than 3 parameters.
These parameters should have the following properties:
  parameters in an icon should be easily combinable.
  parameters should be separately perceivable.
  icons should differ significantly if the coded parameters differ.
The development of effective geometric codes is not trivial!
One of the first (and most well-known) icons is the Chernoff face (Chernoff 1973).
It codes 12 variables in the form of head, nose, mouth, eyes

## Slide 78: Visualization of Multiparameter Data

## Slide 79: Visualization of Multiparameter Data
Further examples
  data jacks (Cox, Ellson, Olano)
  3-dimensional figures consisting of 4 elements
  data values are coded in color and length of these elements.

## Slide 80: Visualization of Multiparameter Data
Further examples
  m-arm-glyph, stick figures (Pickett, 1970; Pickett & Grinstein, 1988)
  2-dimensional figure with m arms; data values are coded in
    Length,
    Width, and
    Angle to main axis
  of the arms.

## Slide 81: Visualization of Multiparameter Data
Stick figure example:

## Slide 82: Visualization of Multiparameter Data
Color icon (Levkowitz)
  uses color, shape, and texture features;
  data values are coded
    in linear feature (edges, diagonal), or
    in triangles.
Circle arrangements
  codes data values in size and color of circles

## Slide 83: Visualization of Multiparameter Data
Shape coding (Beddow, 1990)
  Icon is a rectangle containing a regular grid. Each grid cell is used for one parameter.
  The value of the parameter is coded in color.
  The rectangular icons are usually placed row-wise. Hence, certain order criteria can be considered. (temporal or spatial correlations, ordering according to special data values).

## Slide 84: Visualization of Multiparameter Data
Spiral shaped arrangement of a car glyph
  The rectangular icons are usually placed row-wise.
   Other configurations of the icons are possible. (spiral shaped configuration, grouping techniques, Keim, Kriegel, 1994)

## Slide 85: Visualization of Multiparameter Data
ShapeVis (Theisel/Kreuseler 98)
  Based on enhanced spring model
  Classic spring model (Problems: ambiguity, insensitivity to coordinate scaling):
    Every dimension is represented by a dimension point di (i=1..m) on a sphere
    An observation case O=(c1,...,cm) is represented by a point p
    Springs from p to di with the stiffness ci  search for position of balance of p.

## Slide 86: Visualization of Multiparameter Data
Solution: observation case described by points p,p1,...,pm:
Then construct surfaces out of p,p1,...,pm in such a way that an observation case is uniquely described by its location, size and shape.

## Slide 87: Visualization of Multiparameter Data
Overview
Example: car data set

## Slide 88: Visualization of Multiparameter Data
Zoom into a cluster
Example: car data set

## Slide 89: Visualization of Multiparameter Data
Assessment of icon based techniques
  good:
    perception of parameter correlation and groupings possible;
    icons can be positioned in observation space;
    big data sets can be handled.
  bad:
    hard to identify particular data
    (exception: nominal parameters with small range)

## Slide 90: Visualization of Multiparameter Data
Pixel oriented techniques
  Idea:
  visualization of data values as color coded pixels; color coding of the data values is done in a separate window for each parameter.
   visualization of large data sets possible.
  Arrangement of the pixels has to be specified:
    Row-wise
    Column-wise
    Other patterns

## Slide 91: Visualization of Multiparameter Data
2 step techniques:
  pixels organized in small groups
  arrangement of the groups
Recursive pattern technique (Keim, Kriegel, 1995)
  recursive arrangement of the groups

## Slide 92: Visualization of Multiparameter Data
Example for recursive pattern technique: A measurement station yields 5 parameters three times daily: air pressure, humidity, temperature, O2- and CO2 concentrations.
Pixel arrangement:
  1st level: create a 3 * 5 pattern which codes the daily measures row-wise.

## Slide 93: Visualization of Multiparameter Data
2nd level: create a 5 * 7 pattern which codes measured values of a month in a weekly left-right-arrangement.

## Slide 94: Visualization of Multiparameter Data
3rd level: create a 20 * 12 Pattern with the measured values of 20 years; monthly in a left-right-arrangement

## Slide 95: Visualization of Multiparameter Data
Result: image of 300 * 420 pixels representing 126000 data values

## Slide 96: Visualization of Multiparameter Data
Stock prices of the FAZ index , Jan 74 – April 95
Example:

## Slide 97: Visualization of Multiparameter Data
Assessment of pixel based techniques
  good
    visualization of big data sets possible
  bad:
    effective arrangements are necessary
    problems with color perception and distinction on pixel level

## Slide 98: Visualization of Multiparameter Data
Hierarchical methods
  Principle: visualization of data values using hierarchical parameter arrangements

## Slide 99: Visualization of Multiparameter Data
Dimensional stacking (Leblanc, Ward, Wittels, 1990)
starting point:
m parameters P1 to Pm with m cardinal numbers K1 to Km
(cardinal number = number of classes in the domain of each parameter)
idea: define pairs of parameters and combine them
steps:
  choose the most important parameters Pi, Pj; define a 2D grid Ki x Kj;
  recursive subdivision of each grid cell using the next pairs of parameters;
  color coding of the final grid cells using:
  the value of a dependent parameter
  or
  the frequency of data in each grid cell

## Slide 100: Visualization of Multiparameter Data
Example 1:
5-dimensional parameter set (P1=location, K1=3; P2=time, K2=4; P3=agent, K3=4; P4=customer group, K4=4; P5=exchange, K5=10)
build pairs of parameters out of P1 ,..., P4,
color code P5

## Slide 101: Visualization of Multiparameter Data
Example 2:
  microbiological data set
  define pairs of parameters
  color code: frequency

## Slide 102: Visualization of Multiparameter Data
Problems:
  effective definition of the parameter pairs
  effective partition
  level of recursion

## Slide 103: Visualization of Multiparameter Data
Worlds-within-Worlds (Feiner, Beshers, 1990)
Approach similar to dimensional stacking:
  choose a triple of parameters; defines a 3D coordinate system;
  choose a point in this coordinate system; define another coordinate system by choosing three more parameters at this point;
  define triples of parameters and coordinate systems recursively;
  visualize values in the last-defined coordinate system.

## Slide 104: Visualization of Multiparameter Data
Worlds-within-Worlds (Feiner, Beshers, 1990)

## Slide 105: Visualization of Multiparameter Data
Assessment of hierarchical methods:
  good:
    supports level of detail (LOD) and focusing
    switch between overview and detail visualizations possible
  bad:
    effective parameter pairing & ordering has to be given / created

## Slide 106: Visualization of Multiparameter Data
Summary
Consider the techniques concerning the following fundamental aims:
  perceive relations between parameters,
  identify individual values.

## Slide 107: Visualization of Multiparameter Data
This tables shows only a trend. Reasons for this are:
  Methods in each group differ
  Annotation plays a role
  Interaction issues play a role
Can exact values or additional information be obtained by mouse-clicking?
  Can axes be scaled or replaced ?
  Is data set interactively reducible?
  Are selections possible ?
  ...
Another problem is the treatment of missing values:
  Do not display them (e.g., background color for pixel-oriented techniques)?
  Special treatment of missing values?

## Slide 108: Visualization of Multiparameter Data
Visualization of the Observation Space

## Slide 109: Visualization of Multiparameter Data: Observation Space
Visualization of the spatial context
  Here we consider the visualization of the dimensions of the observation space, which define a spatial coordinate system.
  Aim: show the correlations between data values and their spatial position.

## Slide 110: Visualization of Multiparameter Data: Observation Space
3 cases can be distinguished (relating to the 3 types of impact areas) (see Robertson):
  point context correlation between data values and particular points in observation space (i.e. measured values per observation point in a lake)
  local context
  data values in a local environment (i.e. data values in the northern part of the lake)
  global context
  distribution of data values in the whole observation space (i.e. data values for the whole lake)
  Here we consider n=2 and n=3. (grid dimensionality)

## Slide 111: Visualization of Multiparameter Data: Observation Space
Two kinds of representing the spatial context:
  Direct spatial context
  observation space and data values are shown in one visual representation; correlations are realized by positioning.
    Intuitive perception of spatial context;
    Limited number of values can be visualized.
  Indirect spatial context
  observation space and data values are shown in different visual representations; correlations are realized using special encodings (color; annotations, ...)
    spatial context perceivable but not as intuitively as in direct spatial context;
    larger number of values can be coded.
  Combination of direct and indirect representation of spatial context

## Slide 112: Visualization of Multiparameter Data: Observation Space
Direct representation of spatial context

## Slide 113: Visualization of Multiparameter Data: Observation Space
Indirect representation of spatial context

## Slide 114: Visualization of Multiparameter Data: Observation Space
Indirect representation of spatial context

## Slide 115: Visualization of Multiparameter Data: Observation Space
Combination indirect/direct spatial context

## Slide 116: Visualization of Multiparameter Data: Observation Space
Visualizing the temporal context
If one dimension of the observation space is the time axis, the data set has a temporal context.
Representation of temporal context is not necessarily related to the physical „time“.

## Slide 117: Visualization of Multiparameter Data: Observation Space
Temporal context: We distinguish between
Temporal context of the data
  data which changes over time (dynamic data)
  data which does not change over time (static data)
  data which is constant in sufficiently small periods (quasi-static data)
Temporal context of the graphical representation
  visual representations which change over time (dynamic representations)
  visual representations which do not change over time (static representations).
All combinations between temporal content and graphical representation are possible and make sense: see following examples

## Slide 118: Visualization of Multiparameter Data: Observation Space
Static representations for:
Static data
  If the data does not change over time, a static representation is adequate.
  A temporal context can be represented by an annotation. (e.g., time of data observation; time interval in which data are valid)
Dynamic data
  Static representations are appropriate for dynamic data especially if quantitative statements are to be given (e.g., time diagrams, time axis in parallel coordinates, multi-window-techniques, special icons).
Quasi-static data
  For quasi-static data, quasi-static representations are appropriate; examples: Worm Plots (Treinish et al., 1997).

## Slide 119: Visualization of Multiparameter Data: Observation Space
Worm Plots (Treinish et al., 1997)
“scatterplots connected over time”
Construction of a circle in a time step
Construction of a worm over several time steps

## Slide 120: Visualization of Multiparameter Data: Observation Space
Dynamic representations for:
Static data
  If the static data too complex to be represented in one static representation: dynamic representation is an alternative.
Dynamic data
  Dynamic representations are appropriate for dynamic data. Animated image sequences show parameter changes and trends (e.g., animated flow visualization using particles).
Quasi-static data
  Representation must not show more dynamics than in the data.

## Slide 121: Visualization of Multiparameter Data: Observation Space
Example: Topological flow visualization (dynamic data)
dynamic representation  dynamic data  static representation

## Slide 122: Visualization of Multiparameter Data: Observation Space
Visualization of abstract dimensions
  Observation space may contain dimensions with neither spatial nor temporal context.
  These dimensions are called abstract dimensions.
  Abstract dimensions are defined to:
    compare and order data sets (introduce ordering number);
    simplify data sets (use city or area names instead of a geographical reference system) or
    show higher-dimensional dependencies.
  For visualizing abstract dimensions, methods for multivariate data can be used. Distinction between these abstract dimensions and dependent variables should be possible.

## Slide 123: Visualization of Multiparameter Data: Observation Space
Example for abstract dimensions
abstract dimension:
counties in a region of Germany; abbreviated by their license plate number
number of infections