## Slide 1: Flow Visualization
Problems and Concepts
Elementary Methods Characteristic Curves
Geometry-Based Methods

## Slide 2: Flow Visualization: Problems and Concepts
Flow data appear in a variety of applications, i.e.
  Simulation / computation of flow around cars, planes, ships
  atmospheric flow for weather forecast
  studying flow in bottling / filling devices
There are different aims, such as:
  perceiving and understanding physical phenomena
  modeling of flow processes
  optimization in technical design
  search for damage reasons

## Slide 3
Smoke angel
A C-17 Globemaster III from the 14th Airlift Squadron, Charleston Air Force Base, S.C. flies off after releasing flares over the Atlantic Ocean near Charleston, S.C., during a training mission on Tuesday, May 16, 2006. The "smoke angel" is caused by the vortex from the engines. (U.S. Air Force photo/Tech. Sgt. Russell E. Cooley IV)

## Slide 4: Flow Visualization: Problems and Concepts
A wind tunnel model of a Cessna 182 showing a wingtip vortex. Tested in the RPI (Rensselaer Polytechnic Institute) Subsonic Wind Tunnel. By Ben FrantzDale (2007).

## Slide 5: Flow Visualization: Problems and Concepts
wool tufts
http://autospeed.com/cms/A_108677/article.html
http://autospeed.com/cms/A_108677/article.html
Notes: 5

## Slide 6: Flow Visualization: Problems and Concepts
smoke nozzles
smoke injection
[NASA, J. Exp. Biol.]
smoke nozzles
http://autospeed.com/cms/A_108677/article.html
http://autospeed.com/cms/A_108677/article.html

## Slide 7: Flow Visualization: Problems and Concepts
Smoke injection
A. L. R. Thomas, G. K. Taylor, R. B. Srygley, R. L. Nudds, and R. J.
Bomphrey. Dragonfly flight: free-flight and tethered flow visualizations
reveal a diverse array of unsteady lift-generating mechanisms, controlled
primarily via angle of attack. J Exp Biol, 207(24):4299–4323, 2004.
Notes: 7

## Slide 8: Flow Visualization: Problems and Concepts
http://de.wikipedia.org/wiki/Bild:Airplane_vortex_edit.jpg
Notes: 8

## Slide 9: Flow Visualization: Problems and Concepts
Smoke injection
http://www-me.ccny.cuny.edu/research/aerolab/facilities/images/wt2.jpg
Notes: 9

## Slide 10: Flow Visualization: Problems and Concepts
Clouds (satellite image)
http://de.wikipedia.org/wiki/Bild:Vortex-street-1.jpg
Juan Fernandez Islands
Notes: 10

## Slide 11: Flow Visualization: Problems and Concepts
http://daac.gsfc.nasa.gov/gallery/frances/
Clouds (satellite image)
Notes: 11

## Slide 12: Flow Visualization: Problems and Concepts
flow data; a) on regular grid; b) scattered flow data
Flow data:
  vector data on a 2D or 3D grid
  in addition scalar data may be defined per grid point
  ( EV2[2] , EV3[3])

## Slide 13: Flow Visualization: Problems and Concepts
Obtaining flow data:
  by measurement:
    sensors at certain sample points of a fluid/gas in motion give flow velocity at these points
    optical methods: PIV
  by simulation: solving the Navier/Stokes equations

## Slide 14: Flow Visualization: Problems and Concepts
simulation / measurement
flow data
interpolation
vector field
visualization
Flow data is converted to a vector field by interpolation of the vectors inside the cells.

## Slide 15: Flow Visualization: Problems and Concepts
scalar field
vector field
tensor field
2D vector field
Jacobian of 2D vector field

## Slide 16: Flow Visualization: Problems and Concepts
vector field
tensor field
2D vector field
Jacobian of 2D vector field
Supposed to be continuous and differentiable. This means we can compute its partial differentials and write them into the 2x2 matrix:

## Slide 17: Flow Visualization: Problems and Concepts
vector field
parameter-independent
one-parameter-dependent
steady vector field
unsteady vector field

## Slide 18: Flow Visualization
Visualization methods for flow fields

## Slide 19: Flow Visualization: Problems and Concepts
information encoded in a vector
orientation
direction
length / velocity
vector field visualization method:
which of these aspects are shown?

## Slide 20: Flow Visualization: Visualization Methods
Methods for flow data:
  Elementary (direct) methods: show properties of selected points
  Geometry-Based Methods: integrated lines, surfaces
  Image-Based Methods: use textures to show the flow
  Feature extraction: focus on specific aspects/features of the flow
    Topology-based flow visualization
  Further methods
Main problems for visualization:
  spatial complexity
  dimensionality of the data

## Slide 21: Flow Visualization
Elementary (Direct) Methods

## Slide 22: Flow Visualization: Elementary Methods
Elementary Methods:
Present the complete data set at low level of abstraction
Mapping is direct, without complex conversions or extractions
3 main representations:
  color coding
  arrow plots
  icons
 very frequently used
Notes: 22

## Slide 23: Flow Visualization: Elementary Methods
Color Coding:
Extract scalar field from vector field (i.e. magnitude, curvature, pressure, temperature)
2D: direct color coding to visualize them
same for slices or boundary surfaces in 3D
3D  volume visualization (FlowVis  VolVis)
 loss of information

## Slide 24: Flow Visualization: Elementary Methods
Examples for Color Coding:
www.fluent.com

## Slide 25: Flow Visualization: Elementary Methods
Volume illustration for flow visualization [Svakine et al 05]

## Slide 26: Flow Visualization: Elementary Methods
Arrow plots:
also called hedgehog plots
represent velocity as arrows at regular locations, e.g., place arrows at grid points
 overloading possible
arrows: (scaled) unit length or encode magnitude
well-established for 2D

## Slide 27: Flow Visualization: Elementary Methods
[Kirby et al 99]: multiple values of 2d flow data by layering concept related to painting process of artists

## Slide 28: Flow Visualization: Elementary Methods

## Slide 29: Flow Visualization: Elementary Methods
3D arrow plots:
Occlusion problem  careful seeding
Ambiguity problem
Solutions:
  3D icons (cylinder + cone)
  Highlight parts of error plot which points into a user defined direction

## Slide 30: Flow Visualization: Elementary Methods

## Slide 31: Flow Visualization: Elementary Methods
[Schulz et al 99]

## Slide 32: Flow Visualization: Elementary Methods
Icons:
Place icon at selected locations and encode different values of the flow
Seeding strategy necessary (usually interactive)
Example: probe for local flow visualization [de Leeuw, van Wijk 93]

## Slide 33: Flow Visualization: Elementary Methods
Show in Amira:
  Color Coding
  Arrow plots
  3D Vectors
  Local Probe

## Slide 34: Flow Visualization
Characteristic Curves (Integral Curves)
very important

## Slide 35: Flow Visualization: Characteristic Curves
A tangent curve s(t) of the vector field v is a curve in E2/3 with the property:
for any t of the domain of s.
Interpretation: path of a massless particle in a flow described by v
denotes the tangent vectors of s(t)
very important

## Slide 36: Flow Visualization: Characteristic Curves
Properties of tangent curves:
Tangent curves do not intersect each other (except for critical points of v) .
Given a point in the vector field v, there is one and only one tangent curve through it (except for critical points of v)
A parametric description of stream lines is usually not possible.
  But it is possible for linear vector fields.
very important

## Slide 37: Flow Visualization: Characteristic Curves
Based on tangent curves, we define 4 types of characteristic curves of a vector field
very important
concept of
tangent curves
concept of
characteristic curves
stream lines
path lines
streak lines
time lines

## Slide 38
2D time-dependent vector field
particle visualization

## Slide 39
stream lines
path lines
curve parallel to the vector field in each point for a fixed time
describes motion of a massless particle in an steady flow field
curve parallel to the vector field in each point over time
describes motion of a massless particle in an unsteady flow field

## Slide 40: Flow Visualization: Characteristic Curves
steady vector field
unsteady vector field
stream lines
stream lines
path lines
very important

## Slide 41: Flow Visualization: Characteristic Curves
steady vector field
unsteady vector field
3D
2D
nD unsteady vector field  (n+1)D steady vector field
very important

## Slide 42
streak line
location of all particles set out at a fixed point at different times

## Slide 43
stream lines
path lines
streak lines

## Slide 44
time line
location of all particles set out on a certain line at a fixed time

## Slide 45
time line
location of all particles set out on a certain line at a fixed time

## Slide 46
stream lines
path lines
streak lines
time lines

## Slide 47: Flow Visualization: Characteristic Curves
Characteristic curves of a vector field:
Stream line: curve tangential to the vector field in each point for a fixed time
Path line: describes the motion of a particle over time in an unsteady flow field
Streak line: location of all particles set out at a fixed point at different times
Time line: location of all particles set out on a certain line at a fixed time
very important

## Slide 48: Flow Visualization: Characteristic Curves
Stream and Path lines:
  Through all non-critical points (x,t) in space-time there is exactly one stream/path line passing through it.
Streak and Time lines:
  Many streak/time lines through every point (of the spatial domain)
   makes it difficult to describe streak/time lines as tangent curves of some vector field
    But it is possible. We may discuss it in a later session.
Stream, Path, and Streak lines coincide in a steady vector field.
very important

## Slide 49: Flow Visualization: Characteristic Curves
stream path
streak time
Example:
v(x,t) = (1-t) + t
Show in Amira

## Slide 50: Flow Visualization: Characteristic Curves
Characteristic curves of a vector field:
  Stream line: P0, P1, P2
  Path line: P0, P1, P4
  Streak line: P0, P3, P4

## Slide 51: Flow Visualization: Characteristic Curves
A time-dependent (unsteady) vector field

## Slide 52: Flow Visualization: Characteristic Curves
Stream line
curve tangential to the vector field in each point for a fixed time

## Slide 53: Flow Visualization: Characteristic Curves
solution
Stream line
curve tangential to the vector field in each point for a fixed time

## Slide 54: Flow Visualization: Characteristic Curves
Path line motion of a particle over time in an unsteady flow field

## Slide 55: Flow Visualization: Characteristic Curves
Path line motion of a particle over time in an unsteady flow field

## Slide 56: Flow Visualization: Characteristic Curves
Path line motion of a particle over time in an unsteady flow field
solution

## Slide 57: Flow Visualization: Characteristic Curves
Streak line
location of all particles set out at a fixed point at different times

## Slide 58: Flow Visualization: Characteristic Curves
Streak line
location of all particles set out at a fixed point at different times
solution
particle started at t=0
particle started at t=1
particle started at t=2
particle “started” at t=3

## Slide 59: Flow Visualization
Geometry-Based Methods
(integration-based)

## Slide 60: Flow Visualization: Geometry-Based Methods
Geometry-based Methods:
Idea: extract geometric objects for which the shape is directly related to the flow
Examples:
  Stream lines
  Streak lines, path lines, time lines
  Stream ribbons
  Stream surfaces
  Streak surfaces, path surfaces, time surfaces

## Slide 61: Flow Visualization: Geometry-Based Methods
Integral curves:
“natural” visualization technique
appropriate stream/path/streak/time lines give immediate insight into the flow
Problems:
  How to integrate these curves?
  Which lines to draw? (seeding)
  Spatial impression in 3D?

## Slide 62: Flow Visualization: Geometry-Based Methods
Integrating stream lines:
  In general: no closed form solution for stream lines
    Exception: linear vector fields (2D and 3D): stream lines can be formulated as parametric exponential curve
    2D quadratic Bezier curves (parabolas) are subclass of stream lines of 2D linear vector fields
    3D non-planar cubic curves are subclass of stream lines of 3D linear vector fields
  Usual way: numerical integration

## Slide 63: Flow Visualization: Geometry-Based Methods
Numerical integration of stream lines:
approximate stream line by polygon xi
Testing example:
  v(x,y) = (-y, x/2)^T
  exact solution: ellipses
  starting integration from (0,-1)
x
y

## Slide 64: Flow Visualization: Geometry-Based Methods
Euler integration:
Idea: xi+1 = xi + s v(xi)
s: step size
Large numerical error!
Error proportional to s2

## Slide 65: Flow Visualization: Geometry-Based Methods

## Slide 66: Flow Visualization: Geometry-Based Methods
Second order Runge Kutta integration:
Idea:
  go half a step forward
  evaluate vector there
  use at starting point
xi+1 = xi + s v(xi + s/2 v(xi))
better than Euler

## Slide 67: Flow Visualization: Geometry-Based Methods
Fourth order Runge Kutta integration:
Standard; better than second order RK
  Resembles the true solution up to s4 (error proportional to s5)
Idea: step is convex
  Combination of 4 vectors
with

## Slide 68: Flow Visualization: Geometry-Based Methods
Adaptive step size for RK4:
Idea: in areas of rather straight flow the step size can be larger than in areas of highly curved stream lines
do RK3  difference between RK4 and RK3 gives estimation for step size
gives

## Slide 69: Flow Visualization: Geometry-Based Methods
Adaptive step size for RK4:
Define error tolerance t. Then optimal step size is:
r>1: safety factor
- ask integrator to compute D with step size s
- If D>t, then repeat current step with step size s*
otherwise proceed and take s = min(s*,smax) for next step
This integration is called RK4(3).

## Slide 70: Flow Visualization: Geometry-Based Methods
Which integrator to take?
Depends on application!
Rules of thumb:
never use Euler!
RK4 or RK4(3) is safe.

## Slide 71: Ingredients and Concepts for a Stream Line Integrator
Input
  vector field v
  seed point
Concepts
  forward / backward Integration
    integrate in v and –v to get the whole stream line
  stop criteria
    number of steps
    arc length
    domain
    zero or low velocity
  arc length parameterized output
    integration in the direction field
Output
  polyline approximating the stream line

## Slide 72: Flow Visualization: Geometry-Based Methods
Seeding of integral lines:
which stream/path/streak/time lines to visualize?
too few: important details get lost
too many: overload, visual clutter
simple approaches:
  start on regular grid points
  start randomly

## Slide 73: Placement Methods for Stream Lines
Jobard et al., 1997
Turk and Banks, 1996
Mebarki et al., 2005
Rosanwo et al., 2009

## Slide 74: Flow Visualization: Geometry-Based Methods
Stream line seeding:
  2D: evenly spaced stream lines
  Turk/Banks 96:
    start with streamlets (very short stream lines)
    apply a series of energy-decreasing elementary operations: combine, delete, create, lenghten, shorten streamlets
    energy: difference between low-pass filtered version of current placements and uniform grey image

## Slide 75: Flow Visualization: Geometry-Based Methods

## Slide 76: Flow Visualization: Geometry-Based Methods

## Slide 77: Flow Visualization: Geometry-Based Methods

## Slide 78: Flow Visualization: Geometry-Based Methods
Stream line seeding:
  2D: evenly spaced stream lines
  Jobart/Lefer 97:
    greedy placement of new stream lines in the neighborhood of already present stream lines
    2 steering parameters dsep, dtest with dtest < dsep
    Start integration of an arbitrary stream line in forward and backward direction until it
      Leaves the domain
      Ends in a critical point
      Comes closer than dtest to another drawn stream line
    Next stream line: starts in a point with distance dsep to first stream line
    Ends when no further stream lines are possible

## Slide 79: Flow Visualization: Geometry-Based Methods

## Slide 80: Flow Visualization: Geometry-Based Methods

## Slide 81: Flow Visualization: Geometry-Based Methods
Stream line seeding 3D:
  evenly-spaced does not make sense
  starting on uniform grid:
[Weinkauf 2003]

## Slide 82: Flow Visualization: Geometry-Based Methods
Stream line seeding 3D:
  evenly-spaced does not make sense
  starting in regions of high vector field curvature (i.e., close to critical points):
[Weinkauf 2003]

## Slide 83: Flow Visualization: Geometry-Based Methods
Show demos in Amira
  Curvature based seeding

## Slide 84
What about path / streak / time lines?
Time lines just as simple as stream lines
But it is a bit more complicated for path and streak lines…

## Slide 85
spatial projection
path lines in a flow behind a cylinder
cusp:
isolated point on the curve
where the tangent has a discontinuity

## Slide 86
space-time
spatial projection
path lines in a flow behind a cylinder

## Slide 87: Intersection-Free Placement of Field Lines
def FieldLinePlacement(nDesiredLines):
ResultLines = []
Pool = IntegrateFieldLines(m) #Initialize with m randomly seeded field lines. default: m = 100
while len(ResultLines) < nDesiredLines:
Pool += IntegrateFieldLines(n) #Get n new randomly seeded field lines. default: n = 30
Pool.SortByLength() #Sort field lines in descending order; longest comes first.
LengthOfLastLongLine = Pool[0].Length()
ResultLines += Pool.pop(0) #Add the currently longest line to the result.
while len(ResultLines) < nDesiredLines:
Pool.CutFieldLinesIntersectingWith(ResultLines) #Intersection-free!
Pool.SortByLength() #Sort field lines in ascending order; longest comes first.
if Pool[0].Length() / LengthOfLastLongLine > x: #default: x = 0.98
ResultLines += Pool.pop(0) #Add the currently longest line to the result.
else:
break #Available field lines got too small. Get new ones.
#Delete small lines from the pool before we add new ones in the next loop.
Pool.RemoveLinesSmallerThan(LengthOfLastLongLine * y) #default: y = 0.5
return ResultLines
intersection-free
long lines
good domain coverage
minimal distance between lines

## Slide 88: Intersection-Free Placement of Field Lines
intersection-free
long lines
good domain coverage
minimal distance between lines

## Slide 89: Intersection-Free Placement of Field Lines
Avoid cusps and cusp-like shapes:
 Voxel bit mask of cusp seeding locations
Allow small number
of (self-)intersections:
 User input

## Slide 90: Flow behind a cylinder
path lines
streak lines

## Slide 91: Double Gyre
streak lines

## Slide 92: Heated cylinder
path lines

## Slide 93: Flow Visualization: Geometry-Based Methods
Getting a 3D impression of 3D stream lines:
  Important for spatial perception
  Gives insight into the data
  Extract data properties

## Slide 94: Flow Visualization: Geometry-Based Methods
Getting a 3D impression of 3D stream lines:
  Problem: normal vector not uniquely defined by geometry
   instead: 2D normal space with infinitely many normals
   How to choose a preferred normal vector?
Image from Ovidio Mallo and Ronald Peikert, ETH Zürich

## Slide 95: Flow Visualization: Geometry-Based Methods
Getting a 3D impression of 3D stream lines:
  Classic approach: stream tubes instead of stream lines
   many triangles!

## Slide 96: Flow Visualization: Geometry-Based Methods
Getting a 3D impression of 3D stream lines:
  Modern approach: Use fragment shaders
  Send triangle strip to GPU
  Orient the strip on the GPU such that it lies in the viewing plane
  Use fragment shader to compute cylinder-like shading & depth
Image from
Visualization with stylized line primitives
Carsten Stoll, Stefan Gumhold
IEEE Visualization 2005

## Slide 97: Flow Visualization: Geometry-Based Methods
Electrostatic field of a Benzene molecule
(from Weinkauf 2002)
Illuminated stream lines (Zöckler et al. 1996):
  Alternative approach: illuminate 1D lines
  estimate normal at each vortex
  shade according to the normal

## Slide 98: Flow Visualization: Geometry-Based Methods
Illuminated stream lines (Zöckler et al. 1996):
[Weinkauf 2003]

## Slide 99: Flow Visualization: Geometry-Based Methods
Particle motions:
  step 1: position a particle in the flow field to define starting point
    There are different strategies to set out particles: box, rake, grid
  step 2: compute motion of the particle concerning the flow field
  step 3: visualize the particle at the passed locations
    particles are represented as points or small circles; attributes like color, transparency, can be used for encoding additional information( pressure, temperature)
Modification with particle tails:
  represent particle positions over more time steps; current position is emphasized.

## Slide 100: Flow Visualization: Geometry-Based Methods
A particle tracer has several parameters:
  Number of initial particles
  Maximum age of a particle (remove particles after some time)
  Number of particles seeded in every time step
  …

## Slide 101: Flow Visualization: Geometry-Based Methods
Show in Amira
  Particles